## Slide 1: Is mechanical compression suitable for atmospheric CO2 utilisation on Mars?
Sam Ross

## Slide 2: Context and State-of-the-Art
Pre-term and Week M1

## Slide 3: Motivation
Returning rockets to Earth requires large masses of propellant
Fundamentals of rocket equation demand extreme masses to Earth orbit
  Gear ratio (mearth orbit/msurface of Mars) is 3-4
Manufacturing propellant in-situ has the potential for mass leverage
  One tonne of chemical plant can produce many tonnes of propellant
All current designs for Martian propellant manufacture utilise atmospheric carbon dioxide as chemical feedstock
Atmospheric density is very low, unsuitable for practical use
  Compression is required

## Slide 4: Martian compression - current state of the art
Some historical work from NASA + contractors
Relatively small quantities/flows required
Emphasis on proving performance at subscale
Historically, mechanical systems rejected
  High mass, power, complexity
Cryocooler/freezer-pump systems preferred
Few recent developments
  MOXIE uses single-stage scroll compressor

## Slide 5: Current state of the art…
Chart: Current state of the art
| 6.2399999999999997E-2 | 0.45833333333333331 | 0.06 | 1.2500000000000001E-2 | 0.5 | 8.7999999999999995E-2 | 0.02 | 0.61899999999999999 | 0.1 | 4.1666666666666664E-2 | 0.45833333333333331 | 0.5 | 8.3000000000000004E-2
Cryocooler | 28846.1538 | 3173.2364 | 24000 | 3135.6 | 4435.2 | 19636.3636 | 7200 | 12969.3053 | 3960
Other | 4320 | 5498.1818 | 12888 | 5204.8193

## Slide 6: …is far from what’s required
Chart: Technology required
| 6.2399999999999997E-2 | 0.45833333333333331 | 0.06 | 1.2500000000000001E-2 | 0.5 | 8.7999999999999995E-2 | 0.02 | 0.61899999999999999 | 0.1 | 4.1666666666666664E-2 | 0.45833333333333331 | 0.5 | 8.3000000000000004E-2
Cryocooler | 28846.1538 | 3173.2364 | 24000 | 3135.6 | 4435.2 | 19636.3636 | 7200 | 12969.3053 | 3960
Other | 4320 | 5498.1818 | 12888 | 5204.8193
Cryocooler performance floor | 1196 | 1196
Enthalpy minimum | 41 | 41

## Slide 7: …is far from what’s required
Chart: Technology required
| 6.2399999999999997E-2 | 0.45833333333333331 | 0.06 | 1.2500000000000001E-2 | 0.5 | 8.7999999999999995E-2 | 0.02 | 0.61899999999999999 | 0.1 | 4.1666666666666664E-2 | 0.45833333333333331 | 0.5 | 8.3000000000000004E-2
Cryocooler | 28846.1538 | 3173.2364 | 24000 | 3135.6 | 4435.2 | 19636.3636 | 7200 | 12969.3053 | 3960
Other | 4320 | 5498.1818 | 12888 | 5204.8193
Cryocooler performance floor | 1196 | 1196
Enthalpy minimum | 41 | 41
NASA reference architecture (DRA5)
SpaceX refuelling requirement

## Slide 8: Perceived issues with mechanical compression
High power
Sensitive to dust
Heavy

## Slide 9: Perceived issues with mechanical compression
High power
  Comparison to roughing pumps (piston) usually made
  Testbed scales – mechanical does perform badly!
  Current state of art isn’t especially low power either
Sensitive to dust
Heavy

## Slide 10: Ts diagram generation
Week M1 + M2

## Slide 11: Approach
CoolProp Python interface
Good at evaluating properties above triple point
Reduced functionality below this point
  Phase must be forced to be gas
  Cannot do arbitrary property -> property evaluations
Evaluation near sublimation line: compare to literature
  Vukalovich and Altunin, Thermophysical Properties of Carbon Dioxide
  Enthalpy, entropy, density on sublimation line
  No equations of state for sub-triple behaviour

## Slide 12: Sublimation line

## Slide 13: Methods for building Ts diagram
Direct evaluation on gridlines
Evaluate h(T,s) and p(T,s)
Effective and quick to evaluate
Limited range
  Above triple point temperature only
Reverse evaluation, interpolation
Evaluate s(T, p) and h(T, p)
Invert and interpolate p(s) and h(s) at each value of T
Slow, breaks down below sublimation line
Can produce a value across entire range
  Not always physical

## Slide 14: Output of each method
Direct evaluation
Reverse evaluation and interpolation

## Slide 15: Combined output

## Slide 16: Operating envelope
Weather
Night

## Slide 17: Combined Ts diagram - comments
Reverse method maintains accuracy above triple point
  Reasonable confidence in method
Reverse method distortion is entirely out of the working regime
Combined output can be used to produce lookup tables

## Slide 18: System components
Week M1+M2

## Slide 19: Component efficiencies
Axial compressors
  PR ~1.1, η~89%
Centrifugal compressors
  PR ~3, η~83%
Reciprocating compressor
  PR~3-6, η~78%
Duct
  Variable pressure drop, O(1%)
Heat exchanger
  Variable pressure drop, O(3%) for IGT intercooler
Cyclone separator
  Variable pressure drop, O(6-9 x dynamic pressure)
Inertial Particle Separator
Electrostatic precipitator
  Same model as duct

## Slide 20: 0th order model
Compression energy from stage inlet and outlet temperatures
  800mbar -> 13 bar
  =1.33
  No pressure drops in secondary systems
HX performance is a key parameter
In comparison to cryocoolers
  Best observed is 3153kJ/kg (7.6x worse)
  Performance floor is 1196kJ/kg (2.9x)
 |  | HX cold temperature |  |  |  |  |  | 
 |  | 210 | 220 | 230 | 240 | 250 | 260 | 270
HX hot temperature | 250 | 349.3 | 357.3 | 365.2 | 373.0 |  |  | 
 | 260 | 356.4 | 364.6 | 372.6 | 380.4 | 388.2 |  | 
 | 270 | 363.5 | 371.7 | 379.8 | 387.8 | 395.7 | 403.4 | 
 | 280 | 370.5 | 378.8 | 387.0 | 395.1 | 403.0 | 410.9 | 418.7
 | 290 | 377.4 | 385.8 | 394.1 | 402.3 | 410.3 | 418.3 | 426.1
 | 300 | 384.2 | 392.7 | 401.1 | 409.4 | 417.6 | 425.6 | 433.5
 | 310 | 390.9 | 399.6 | 408.1 | 416.4 | 424.7 | 432.8 | 440.8
 | 320 | 397.6 | 406.4 | 414.9 | 423.4 | 431.7 | 440.0 | 448.1
 | 330 | 404.2 | 413.1 | 421.7 | 430.3 | 438.7 | 447.0 | 455.2
 | 340 | 410.8 | 419.7 | 428.5 | 437.1 | 445.7 | 454.1 | 462.3
 | 350 | 417.3 | 426.3 | 435.2 | 443.9 | 452.5 | 461.0 | 469.4
 | 360 | 423.7 | 432.8 | 441.8 | 450.6 | 459.3 | 467.9 | 476.3
 | 370 | 430.1 | 439.3 | 448.4 | 457.3 | 466.0 | 474.7 | 483.2

## Slide 21: Ts diagram – now tabulated

## Slide 22: Arbitrary process plotting

## Slide 23: Preliminary sensitivity analysis
Machine properties fixed – vary Pout
Baseline assumptions
  First unit PR=2.1 (8 axials)
  Each subsequent PR=2.4 (centrifugal)
  Axials η=89%
  Centrifugals η=83%
  Intercooling to 250K
  5% pressure loss in intercoolers
Intercooler temperature is critical parameter, then inlet temperature
Variable | Output p | Specific work (kJ/kg) | Change
Baseline | 6.37 | 409.7 | 
Ideal machines | 8.67 | 340.2 | -16.96%
η-10% first unit | 6.37 | 416.1 | 1.56%
η-10% last unit | 6.37 | 417 | 1.78%
IC pressure drop +10% | 6.17 | 408.8 | -0.22%
IC pressure drop -10% | 6.79 | 411 | 0.32%
Inlet T +10% | 6.37 | 418.3 | 2.10%
Inlet P -10% | 5.79 | 409 | -0.17%

## Slide 24: Martian system – bits and pieces
Week M2+M3

## Slide 25: CO2 nuance
Different value of 
  Max pressure ratio in centrifugal is ~94% that for air
  Speed of sound is 78% of air, lower choke speed
First stages: relatively close to sublimation line
  Possible limits on diffusion factor to prevent icing
  Margin is ~40K at low pressure, ~40K at high pressure, less inbetween

## Slide 26: Machine scaling framework
Calculation of Reynolds number based on specific speed/diameter for each machine type
Simple efficiency scaling (Re^x)
Suggests highest Reynolds number at inlet (large diameter)
Higher efficiency for higher flow machines
Many many assumptions
  Arbitrary blade speed
  Arbitrary loading
  Arbitrary scaling

## Slide 27: Radiator merit
Basic calculation for radiator effectiveness
Proportional to T/L
Higher temperature = more effective
Greater delta = less effective
Proposed point (330K-250K) is at merit ~0.28, 43% of maximum

## Slide 28: Donald Rapp, “Use of extraterrestrial resource for human space missions to Moon or Mars”
2018 literature review book by NASA ISRU specialist
Some additional insights
Revises performance floor for cryocoolers up by 2.5x, 2900kJ/kg
  Current systems are performing at 93% of theoretical
  0D scaling estimates 6x energy reduction versus theoretical
“Soft floor” for zeolite-based sorption pumps with current technology
  16% w/w CO2 adsorption, 250K temperature swing
  1445kJ/kg CO2
  5 cycles per day –> 1000kg/day = minimum 1250kg of zeolite

## Slide 29: Rapp: atmospheric dust properties
Cites Deirmendjian haze model
  Validated by Curiosity MSL data (Lemmon et al, 2018)
Average particle radius 0.66m
Mass-weighted average radius 2.5m
Average 4 particles per cubic centimetre
  Dust storm condition: order of magnitude higher, larger particle sizes
1.5E+08 particles per kg CO2
14g of dust per kg CO2
5kg dust per year of operation

## Slide 30: Weight estimation
Week M2, M3, M4

## Slide 31: Weight estimation
Axial compressor: Sagerser scaling laws
Centrifugal compressor: model casing and cone weight only
  Assume circular profile, include some crude margin for diffuser
  Thicknesses set by pressures
Heat exchanger: surface area based on required heat transfer
  Reynolds scaling of gas stream only
Motors: based on electric aircraft design formulae
Cryocooler: comparison of current space-grade systems
Freezer structure: geometric scaling

## Slide 32: Weight estimation: assumptions
Centrifugal outlet blade height >2mm (larger better)
Stage efficiency falls into the machine
Motor speed < 100,000RPM
Density inputs from Ts diagram used
Centrifugal inlet radii set by specific diameter rules
HX: 0.5mm wall thickness, 5mm diameter tubes

## Slide 33: Weight assumption: results @ 50g/s
330kg system weight
40kW system power
Cryocooler comparison
  8600kg system
  259kW
Compares very favourably
  96% weight, 85% power reduction
Equivalent System Mass
  Cryocooler 78,530kg
  Turbomachine 8,500kg (89% reduction)

## Slide 34: Waste heat utilisation
Week M5

## Slide 35: Waste heat utilisation
Extracted heat during compression: 370kJ/kg @280K average
During liquefaction: 345kJ/kg @210K average
Stoichometric ice: all values per kg CO2
Energy to heat ice to melting point: 136kJ/kgeq @254K average
Energy to melt ice: 273kJ/kgeq @273K
Ice heat + melt provides 110% of heat sink for compression
  57% of heat sink for compression + liquefaction

## Slide 36: Waste heat utilisation
Ice heat + melt provides 110% of heat sink for compression
  57% of heat sink for compression + liquefaction
Practicality for utilisation depends on extraction architecture
  In-situ thermal mining: probable makes it impossible
Opportunities for “cycle subchilling” seem very promising
13% energy savings from dropping intercool temperature by 10K
Good question for Paul Wooster (SpaceX) in end-of-term update

## Slide 37: Example WHU cycle
Intercool temperature is greater of 210K, 40K above sublimation line
10% energy savings
12% cooling savings
  Potentially reduce heat rejection ESM by 50% or more
  Water melt system already required, no additional system mass
At least 10% ESM savings
With optimistic heat rejection mass reductions: 22% ESM savings

## Slide 38: ESDU 92013 – Heat Exchangers
Air-cooled HX – suggests ΔT>15K
Typical air cooled HX might be 25mm OD steel tubes with 50mm aluminium fins
Crossflow HX: Mean temp difference = 0.7*LMTD
Standard values for U
  Shell/tube with “process water”: 100W/m2K with “low pressure gas”
  Plate/fin with “low viscosity hydrocarbon liquid”: 260W/m2K
  Air-cooled: 700W/m2K with “treated water” - adjust down for density

## Slide 39: Proposed next steps
Week M5, M6

## Slide 40: Proposed solution search architecture

## Slide 41: Single-component ESM optimisation!
Optimisation of geometric parameters to reduce ESM of one component
Comparison of components at a given performance (900Pa, 190K input)

## Slide 42: Cycle generation from architecture

## Slide 43: System designer GUI

## Slide 44: Extreme examples
Real mass is small fraction of ESM
  Baseline: 4.4% is mass, 1.1% is comp!
Reduce ESM: reduce power and cooling demands
Increase number of intercoolers
Mass of HXs is fairly invariant with #
10 ICs: 11xPR1.9 units
25 ICs: 26xPR1.3 units
  Would this be 220kg heavier?
Component efficiency |  | 70% | 
Intercooler pressure drop |  | 0.05%/K | 
Mechanical efficiency |  | 80% | 
Input pressure, temperature |  | 900Pa, 180K | 
Target pressure, temperature |  | 6 bar, 220K | 
Number of intercoolers | 2 | 10 | 25
Flow work kJ/kg | 554.4 | 476.3 | 461.3
Total cooling kJ/kg | 502.3 | 462.7 | 448.5
Power ESM kg | 4193 | 3602 | 3490
Cooling ESM kg | 3742 | 3447 | 3341
Power + cooling ESM kg | 7935 | 7049 | 6831
Improvement (kg) | 0 | -886 | -1104

## Slide 45: Solving equations to optimise mass
Not friendly!

## Slide 46: Order of magnitude mass scaling
W=17.9kg
In contrast
  d(efficiency)/d𝜓 ~ 3-10%
  d(efficiency)/d𝜙 ~ 1%
1% change in efficiency ~ 1% change in power
Power is ~40% of ESM
Therefore
  𝜓 1->2: Weight -0.5kg, efficiency -3%, power +3%
  ESM weight -0.1%, ESM power +1.2%
Almost always best to go for optimal efficiency

## Slide 47: Scipy optimisation
Week M7, M8

## Slide 48: Scipy optimisation with complex constraints
All optimisers can bound input parameters (, , )
Scipy ‘trust-constr’ allows for better constrained optimisation
Can take arbitrary function calls for constraints on output
  Constraints on derived geometric properties
Seems to respect actual physical limits
PR = 1.36
30% mass reduction

## Slide 49: Radial optimisation
Takes O(2 minutes) per optimisation
  Need to explore speedup options
Very substantial mass reduction, brings to reasonable values
  100-400kg
Seems to be pursuing less aggressive stage loading, higher speed
  =0.85, in line with max efficiency
  10kRPM for highest work stage

## Slide 50: Manual cost function
Move to Nelder-Mead optimisation strategy
Manually input cost function
When some physical limit is exceeded, add constraint mass
Ramps in linearly to aid optimisation
Generally works well but seems to find strange “optimals”
Bladeheight limit kicks in
Limit of performance from Smyth – sets η=1%
PLACEHOLDER

## Slide 51: Effect of new cost function

## Slide 52: Trying to explain behaviour
η=1%
η=28%
Line: η=94%
η=47%
η=63%

## Slide 53: Removing physical mass from optimisation
Line: η=94%
η=1%

## Slide 54: Post-Christmas

## Slide 55: Fixing the optimiser

## Slide 56: Change of initial conditions
Sped up calculation
  Swapped some minimisation for analytic solutions inside calculation
  0.18s per optimisation
Improved initial guesses
Not sure what’s going on with physical weight
Runtime doubles to ~0.37s
???

## Slide 57: Improving compressor optimisation
Determined relationship between parameters for optimal condition
  Not too sure how to make best use of these

## Slide 58: Single equation optimisation

## Slide 59: Reducing to single equations doesn’t seem to work
One equation
Some efficiencies are 94%, still comedically wrong
Two equations, minimising both
Every efficiency is 1%, no clue what’s happening

## Slide 60: Output of optimiser
 | N blocks | PR/stage | Input pressure kPa | Mean inlet radius mm | Outlet radius mm | Bladeheight mm | Speed kRPM | Stage weight kg | Equivalent axial | Equivalent axial kg
Radial | 15 | 1.542 | 0.9 | 64.4 | 83.6 | 38.4/11.6 | 24.7 | 2.91 | 1.45 | 1.45
 | 15 | 1.542 | 100 | 12.1 | 15.5 | 4.18/1.63 | 100 | 0.08 | 39.65 | 39.65
 | 10 | 1.87 | 0.9 | 36.9 | 56 | 26.3/12.7 | 100 | 1.44 | 2.03 | 2.03
 | 10 | 1.87 | 100 | 10.6 | 18.8 | 4.79/1.16 | 100 | 0.14 | 51.73 | 51.73
 | 7 | 2.361 | 0.9 | 46.5 | 71.3 | 49.6/10 | 27.4 | 2.07 | 2.61 | 2.61
 | 7 | 2.361 | 100 | 12 | 48.6 | 4.22/0.73 | 100 | 1.18 | 66.51 | 66.51
Axial |  | PR/stage | Input pressure | Mean radius |  | Bladeheight | Speed | Stage weight |  | 
 |  | 1.1 | 0.9 | 57 |  | 86.9 | 10.9 | 0.29 |  | 
 |  |  | 100 | 255 |  | 3 | 7.2 | 7.39 |  | 

## Slide 61: Issues
Immediately ran into global/local minimum issues
Centrifugal compressors: 5-variable space, local minima likely
  Would be nice to find a way to visualise this
Optimiser seems to get “into a rut”
  Efficiency halts at 30% or less
  Changing initial guess causes dramatic change in output

## Slide 62: Failed solutions! Lots of them

## Slide 63: Basin-hopping
Solution: basin-hopping
  Local minimisation interspersed with “hops”
  Can escape local minima and better find global minima
  Results in a more random process
When number of hops is low, solver is no longer determininstic
  Finds different minima on each usage

## Slide 64: Evolution of the solution

## Slide 65: Basin-hopping characterisation
Chart: ESM evolution with number of basin-hops
| 1 | 2 | 5 | 10 | 20
A | 1.1647 | 1.1379 | 1.0354 | 1.0073 | 1
B | 1.1254 | 1.0345 | 1.0211 | 1.0461 | 1
C | 5.6826 | 1.3311 | 1.0833 | 1.2826 | 1
D | 1.1089 | 0.99519 | 0.97332 | 1.0236 | 1
E | 4.3718 | 1.0305 | 1.0277 | 1.0273 | 1
F | 1.1406 | 1.0008 | 1.0276 | 1.0004 | 1
Chart: Percent above 70% efficiency with number of basin-hops
| 1 | 2 | 5 | 10 | 20
 | 40 | 50 | 100 | 100 | 100
 | 100 | 100 | 100 | 100 | 100
 | 10 | 40 | 50 | 50 | 80
 | 100 | 100 | 100 | 100 | 100
 | 10 | 70 | 90 | 60 | 80
 | 100 | 100 | 100 | 100 | 100

## Slide 66: Optimal number of hops
Time penalty is reasonable considering improvement in performance
N=4 selected for now
Reasonable slowdown
Better performance considering optimality
Chart: Optimisation time with number of basin-hops
| 1 | 2 | 4 | 5 | 10 | 20
Time | 0.37883 | 0.53017 | 0.80367 | 0.946 | 1.4417 | 3.1272
Time to reach 70% efficiency | 1.5233 | 0.80319 | 1.1182 | 1.124 | 1.8227 | 3.4066

## Slide 67: Actual solution

## Slide 68: Nelder-Mead algorithm
Takes a simplex (=N-dimensional triangle) based on input values
Scipy default simplex: vary each value by +5% in turn
But we have well-defined extrema for each dimension
  Practical limits for speed, hub radius, diffusion factor
  Aerodynamic limits for work and flow coefficient
Use these as to create extrema of simplex
Simplex thus spans entire region between 80% of specific speed/diameter-based initial guess and maximum values
Extends to arbitrary dimensions

## Slide 69: Effect of custom simplex
Using Scipy default simplex
0.37s per optimisation
Custom simplex
0.25s per optimisation, 20% reduction in max ESM

## Slide 70: Advanced HX model

## Slide 71: Heat exchanger advanced model
Improved calculations for HX mass and design model
  Thermal resistance from wall and coolant-wall interface
  Pressure drop based on actual data
Thermopedia as secondary source, references listed but not followed through
Coolant pressure drop and pumping power significant factors
Switch to low-viscosity low-temperature coolant fluid
  Therminol VLT
  Explore other options in future – supercritical helium? Liquid CO2?
Notes: Motivated in no small part by REL interview

## Slide 72: Design cases considered
Near-inlet HX
1.9kPa, 230K
50g/s
  1.14m3/s
Flow area from 10cm2 to 10m2
  Velocity from 1140m/s to 0.114m/s
Near-outlet HX
100kPa, 230K
50g/s
  0.0217m3/s
Flow area from 10cm2 to 10m2
  Velocity from 21.7m/s to 2.1mm/s

## Slide 73: Design rules
Max diffusion area of 15
  Limits minimum speed in HX to ~15m/s
  Leads to 4m long diffuser near entry!
Near-entry case: 1.9kPa, 300K, 1.49m3/s
  Inlet area 100cm2
Near-exit case: 100kPa, 300K, 0.028m3/s
  Inlet area 2cm2
1mm copper tubes, 0.1mm wall thickness, 20K difference

## Slide 74: Pressure drop
Much larger problem than previously assumed
High flow velocities from compressor outlet = large losses
Extreme diffusion required to reduce losses
Bringing loss to 5% at HP needs speed of 2.5m/s
  Diffusion ratio of 40

## Slide 75: Underlying reason: very long HX
For 1.9kPa case, pressure drop per tube row is low but number of rows is large
Maximum of 872 tuberows!
New approach
  Parallel-plate heat exchangers with crossflowing fluid
Notes: Parallel plates:
http://www.electronics-cooling.com/2003/05/estimating-parallel-plate-fin-heat-sink-pressure-drop/
Cengel, page 437

## Slide 76: Weight and power model

## Slide 77: New geometry – sintered tubes
SABRE engine precooler – brazed microchannels

## Slide 78: Pressure drop issues resolved

## Slide 79: Higher HTC = less overall weight

## Slide 80: Sintered-wall HX implications
Three design variables
  Coolant speed (0.5-2m/s)
  Gas bulk speed (10-150m/s)
  Row spacing (pitch-to-diameter ratio) (1.25-20)
Low pressure drops with reasonable diffusion
  Can access pressure drop from ~0% to infinity in practice
  No constraint from this system – makes optimisation easier
Low weight
Definitely manufacturable (Reaction Engines)

## Slide 81: Compressor stator modelling

## Slide 82: Axial compressor
ηstator = ηrotor
Maximum ηstage =85%
Target value = 89%
Implies ηstator =97%
Not sure best approach to handle this difference

## Slide 83: Centrifugal compressor
Used rectangular duct diffuser efficiency map
  Assume we always lie on the maximum efficiency line
  Sets L/W, ηstator for a given diffusion factor
Logarithmic spiral blade shape
  Sets L for a given area ratio
Determine all dimensions, number of blades, weight

## Slide 84: Stators in the solver
No effect for axials – no new calculations
Centrifugals
  Adds one additional dimension of optimisation
  Almost no impact on execution speed - 0.4s per design, up from 0.37s
System is making intelligent tradeoffs
  Maximum ηstage for centrifugal is 87% (diffusion factor=15)
  Seems to aim for ηstage ~73% (DF ~ 3.8)
  Reducing emphasis on weight by 20%: aims for ηstage ~81%
  Reducing by 40%: aims for maximal ηstage ~87%
  Apparantly non-linearity in emphasis

## Slide 85: Whole-system optimisation

## Slide 86: Previous baseline
Non-optimised machines
η =85% axials, 73-65% centrifugals
Stator weight, HX weight, HX performance all modelled very crudely
Item | Weight (kg) | Power (kWe) | Cooling (kWe) | ESM (kg)
Compressor weight | 110.2 |  |  | 110.2
HX weight | 239.9 |  |  | 239.9
HX cooling |  |  | 18.5 | 2238.5
Motor weight | 28.3 |  |  | 28.3
Motor power |  | 40 |  | 5960
Batteries |  |  |  | 1111.1
Total | 378.4 | 40 | 18.5 | 9688.0

## Slide 87: Single-item optimisation
Optimise each machine in turn, feeding in parameters from previous
Quick to run
  O(1s) per machine, 19 machines
Definitely not truly optimal
  Diffusers in comp and HX
  Sharing of motors
Slight reduction in ESM but shift from power to physical weight
87.7% ESM reduction vs SotA
ESM table | Weight | Power | Cooling | ESM
Axial compressor | 0.76 |  |  | 0.76
Centrifugal compressor | 88.38 |  |  | 88.38
HX weight | 2445.0 |  |  | 2445.00
HX cooling |  |  | 18577.6 | 2247.89
Condenser weight | 394.16 |  |  | 394.16
Condenser cooling |  |  | 3620.0 | 438.02
Coolant pump weight | 12.69 |  |  | 12.69
Coolant pump power |  | 4277.8 |  | 645.94
Motor weight | 14.85 |  |  | 14.85
Motor power |  | 26335.0 |  | 3976.59
Batteries | 850.35 |  |  | 850.35
Total | 2955.8 | 30612.8 | 22197.6 | 11114.6
Like-for-like total | 2534.1 | 26335 | 18577.6 | 9623.8
Like-for-like change | +569% | -34% | +0.4% | -0.7%

## Slide 88: ESM breakdown in single-item optimised
Chart: 
| Axial compressor | Centrifugal compressor | HX weight | HX cooling | Condenser weight | Condenser cooling | Coolant pump weight | Coolant pump power | Motor weight | Motor power | Batteries
 | 0.76 | 88.375 | 2445 | 2247.8896 | 394.16 | 438.02 | 12.6861 | 645.944 | 14.852 | 3976.585 | 850.3549

## Slide 89: Compressors in single-item optimised design
Machine | Pressure ratio | Inlet mean diameter (mm) | Impeller outlet diameter (mm) | Diffuser outlet diameter (mm) | Bladeheight (mm) | Speed (RPM) | Efficiency | Weight (kg) | Power (W) | ESM (kg-e)
Axial 1 | 1.1 | 68 |  |  | 45.48 | 58327 | 84.6 | 0.16 | 212.5 | 25.873
Axial 2 | 1.1 | 58 |  |  | 37.1 | 100000 | 84.6 | 0.13 | 218.2 | 26.532
Axial 3 | 1.1 | 58 |  |  | 37.17 | 100000 | 84.6 | 0.13 | 224.1 | 27.246
Axial 4 | 1.1 | 58 |  |  | 37.95 | 79791 | 84.6 | 0.12 | 230.2 | 27.974
Axial 5 | 1.1 | 56 |  |  | 35.36 | 100000 | 84.6 | 0.12 | 236.4 | 28.724
Axial 6 | 1.1 | 52 |  |  | 32.52 | 100000 | 84.6 | 0.1 | 242.7 | 29.467
Radial 1 | 2.775 | 71.1 | 117.9 | 869.5 | 19.7 | 45115 | 83.66 | 22.765 | 3020.3 | 388.22
Radial 2 | 2.775 | 86.5 | 102.1 | 841.5 | 7.9 | 48293 | 84.75 | 19.64 | 3344.5 | 424.32
Radial 3 | 2.775 | 36.1 | 49.3 | 639.7 | 6.1 | 100000 | 88.11 | 12.41 | 3216.7 | 401.63
Radial 4 | 2.775 | 30.9 | 97.7 | 653.8 | 2.29 | 100000 | 82.61 | 11.52 | 3431.1 | 426.68
Radial 5 | 2.775 | 25.5 | 66.63 | 634.4 | 0.864 | 100000 | 85.99 | 10.66 | 3296.2 | 409.5
Radial 6 | 2.775 | 20.86 | 90.64 | 656.9 | 0.323 | 100000 | 83.5 | 11.38 | 3395.1 | 422.19

## Slide 90: HX in single-item optimised design
Machine | Pressure ratio | Cooling power (W) | Length (m) | Actual duct length (m) | Coolant pumping power (W) | Number of tube passes | Duct size (mm) | Weight (kg) | ESM (kg-e)
HX 1 | 0.96 | 1894 | 8.424 | 4.09 | 1530.8 | 151478 | 203.6 | 365.3 | 550.53
HX 2 | 0.96 | 3344.5 | 16.97 | 9.56 | 28.01 | 301329 | 170.4 | 170.4 | 173.79
HX 3 | 0.96 | 3216.7 | 7.16 | 4.006 | 459.4 | 168336 | 203.5 | 400.4 | 455.99
HX 4 | 0.96 | 3431.1 | 10.56 | 7.32 | 22.91 | 230706 | 151.6 | 410.5 | 413.27
HX 5 | 0.96 | 3296.2 | 64.2 | 56.5 | 36.8 | 818440 | 81 | 803.7 | 808.15
HX 6 | 0.96 | 3395.1 | 15.4 | 9.55 | 907.3 | 229248 | 108 | 294.7 | 404.48
Condenser | 0.94 | 3620 | 92.63 | 91.94 | 437 | 643552 | 47.6 | 394.16 | 447.04

## Slide 91: Issues seen with single-item optimisation
Heat exchangers are extremely long
  Increase allowable pressure drop per HX - currently an input parameter
  Reduce wall thickness – REL has achieved 40 micron
  Decrease fluid temperature – limits on radiator performance
  Change to a different fluid with better performance
Later stage radials have very small bladeheights, tip gap issues
  Strengthen solver bias away from these values – already very strong
  Increase mass flow to make everything bigger
  Replace final stages with piston/scroll

## Slide 92: HX alternative coolant
Total weight = 2878kg
Total length = 123m

## Slide 93: Alternative coolant – 20 bar supercrit He
Total weight = 2690kg (-6.5%)
Total length = 268m (+118%)

## Slide 94: Alternative coolant – 20 bar liquid ammonia
Total weight = 2649kg (-8%)
Total length = 251.6m (+105%)

## Slide 95: HX alternative coolant – liquid ammonia
Total weight = 2690kg (-6.5%)
Total length = 268m (+118%)

## Slide 96: Diagnosing optimisers failure
All optimisers are failing on HX5, some on HX6
  Maximum number of iterations exceeded
With some experimenting -> massive length excess can occur even when optimiser claims success
Possible approach – switch to minimising pressure drop for a given length, rather than setting pressure drop and finding other parameters
Need to find the ESM effect of high pressure drop

## Slide 97: Crude ESM model
Optimum # of blocks is ~20! For these parameters

## Slide 98: Effect of change in HX pressure drop
With 10 HXs
  8.75%  ESM per %  pressure drop for all HXs -> 0.88% per % per HX
With 15HXs
  12%  ESM per %  pressure drop -> 0.80% per % per HX
20 HXs
  0.78%ESM per %pressure drop per HX
Overall: 0.8% ESM increase per % per HX, 80kg/% pressure drop in HX

## Slide 99: Implementation of variable pressure drop #1
For 50g/s, 1% pressure drop = 80kg weight in the whole system
Just include that in the optimiser
Spits out some really weird results
Output space is probably too steep for Nelder-Mead to handle
Note that true ESM for this component is O(1e3 kg)
Constraints always violated

## Slide 100: Implementation #2
Moving pressure drop into the N-M optimiser doesn’t seem to be effective
Solver always seems to encounter some kind of constraint
Move pressure drop out of the optimiser
Optimise with an input pressure drop, for a sweep of pressure drops
Choose the lowest ESM
Does necessarily involve some slowdown

## Slide 101: Optimiser field with and without pressure drop
Pressure drop calculated from parameters provided
Pressure drop given, penalty applied if doesn’t match target, no constraint, best of 20 pressure drops for overall ESM

## Slide 102: Only difference between these cases
Pressure drop in optimiser
Pressure drop outside optimiser

## Slide 103: Exercise in efficiency maximisation
Bit of a side quest, but a question I’ve wanted to answer for a while
Is it possible to make a truly isothermal compression machine?
Temperature does not deviate from optimal line during compression process

## Slide 104: Physical approach
Cylinder with cooled walls
Piston speed causes fluid to move at Vpiston/2
Fluid motion causes heat loss to walls
Piston also causes compression
Match compression rate to heat loss rate = isothermal compression!
Clearly possible for an infinitestimal period
Possible for continuous flow process? Or impossible

## Slide 105: System behaviour

## Slide 106: Governing equation
Length-diameter ratio of piston governed by speed of piston, temperature, heat transfer
  Role of t? Unclear
For continuous compression, L must decrease continuously
u is gas speed – piston speed is double

## Slide 107: Calculation - t=0.1

## Slide 108: Result
Map of useful outputs
Consider a mid-range system, around 1m in maximum length
Starting at 221K, 10m/s
  Length is 1m
  Want a factor of 10 compression Temperature of 247.5K
  Length should be > 0.1m
Speed must fall to <1mm/s

## Slide 109: Conclusion
Contours of constant length would have to be much shallower for isothermal compression to be effective
Perhaps some very limited regions of effectiveness
These are set by transition between flow regimes – unlikely to be reliable or repeatable
Not a viable idea!

## Slide 110: Documentation for models
All written up
  121 individual equations!
Found one significant mistake
Thermal resistance calculation was messed up
Finding resistance per length of tube, not per surface area
Now fixed, heat exchangers perform much better

## Slide 111: New HX optimisation approach
Lots of things tried, one approach stuck well
Start with a target pressure drop of 1%
Create an optimised heat exchanger
If pressure drop is less than target and heat exchanger volume is less than a certain level -> Accept!
Otherwise, multiply target pressure drop by 1.2
Repeat until target pressure drop is 25%
Works really really well

## Slide 112: Improvement again – 27% ESM reduction
Previous model, 7 HXs
New model, 10 HXs
ESM table | Weight | Power | Cooling | ESM
Axial compressor | 0.76 |  |  | 0.76
Centrifugal compressor | 88.38 |  |  | 88.38
HX weight | 2445.0 |  |  | 2445.00
HX cooling |  |  | 18577.6 | 2247.89
Pre-condenser weight | 394.16 |  |  | 394.16
Pre-condenser cooling |  |  | 3620.0 | 438.02
Coolant pump weight | 12.69 |  |  | 12.69
Coolant pump power |  | 4277.8 |  | 645.94
Motor weight | 14.85 |  |  | 14.85
Motor power |  | 26335.0 |  | 3976.59
Batteries | 850.35 |  |  | 850.35
Total | 2955.8 | 30612.8 | 22197.6 | 11114.6
ESM table | Weight | Power | Cooling | ESM
Axial compressor | 0.76 |  |  | 0.76
Centrifugal compressor | 97.44 |  |  | 97.44
HX weight | 96.68 |  |  | 96.68
HX cooling |  |  | 17841.0 | 2158.76
Pre-condenser weight | 1.61 |  |  | 1.61
Pre-condenser cooling |  |  | 3620.0 | 438.02
Coolant pump weight | 5.01 |  |  | 5.01
Coolant pump power |  | 4.31 |  | 0.65
Motor weight | 17.41 |  |  | 17.41
Motor power |  | 29603.3 |  | 4470.09
Batteries | 822.43 |  |  | 822.43
Total | 218.9 | 29607.6 | 21461.0 | 8108.9

## Slide 113: Results of improved model
Heat exchanger mass back to almost zero
Physical compressor, HX, motor weight is now 2.7% of ESM
Runtime is ~20 seconds!
Approximate total system volume is just 0.804m3
  94% of this is heat exchangers
Speed in heat exchangers is 1-10m/s
Chart: ESM breakdown
| Axial compressor | Centrifugal compressor | HX weight | HX cooling | Condenser weight | Condenser cooling | Coolant pump weight | Coolant pump power | Motor weight | Motor power | Batteries
 | 0.76 | 97.44 | 96.677 | 2158.761 | 1.61 | 438.02 | 5.0054 | 0.651 | 17.4067 | 4470.0907 | 822.4323

## Slide 114: Next problem: small blade spans on radials
Radials still have <1mm exit blade heights
Might be possible to change optimisation goals and avoid these entirely
  Need a good model for efficiency reduction from this effect
If not, more options exist
  Increase mass flow – currently running system for 5.5 hours, can reduce this
  Switch from radial to reciprocating scroll compressor
MOXIE scroll: seems to have ηp = 36%! Not great at all

## Slide 115: Casey and Robinson: different efficiency model for radial compressors
Defines an inlet total flow coefficient
Finds a delta in efficiency from change in Reynolds from a reference value
Scaling depends on inlet flow coefficient
Sign convention such that efficiency drops with lower Reynolds
Our system – Re varies from 0.36Reref to 3.5Reref
Leads to unphysical +100% efficiency of smallest machines

## Slide 116: Alternative, simpler model
Cruder power law scaling
Predicts slightly than first method for larger machines, then sticks to reasonable values elsewhere
Use lower of the two
Chart: Reynolds number efficiency scaling
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Flow coefficient scaling | 0.78724 | 0.82081 | 0.83778 | 0.86018 | 0.867 | 0.87821 | 0.9104 | 1.6545 | 1.7559 | 1.9489
Smyth and Miller | 0.8233 | 0.851 | 0.861 | 0.875 | 0.872 | 0.855 | 0.844 | 0.799 | 0.842 | 0.858
Power law scaling | 0.78276 | 0.82603 | 0.84546 | 0.86728 | 0.86974 | 0.86073 | 0.85912 | 0.84791 | 0.87722 | 0.88933

## Slide 117: Additional corrections
In addition: 0.3% drop in efficiency per 1% relative clearance
Assume minimum clearance – 0.5mm? 1mm?
Exit circumferential Mach number correction – Rusch and Casey
Corrects if M>0.8

## Slide 118: Effect on current design
Reynolds number would increases efficiency on later stages
Tip gap drops efficiency substantially, as expected
Reduction of 3-50% on each stage
Smallest efficiency reduction in middle of system
 |  | Reynolds number scaling |  |  |  |  | Tip clearance |  |  | 
Machine | Smyth η | Phi t1 | Inlet Re | Phi scaling | Power law scaling | New η | Tip gap (mm) | Ratio (%) | Change in η | Final new η
Radial 1 | 82.3% | 0.331 | 53404 | 78.72% | 78.28% | 78.28% | 22.6 | 2.21 | -0.66% | 77.61%
Radial 2 | 85.1% | 0.331 | 69133 | 82.08% | 82.60% | 82.08% | 6.35 | 7.87 | -2.36% | 79.72%
Radial 3 | 86.1% | 0.308 | 88295 | 83.78% | 84.55% | 83.78% | 12.6 | 3.97 | -1.19% | 82.59%
Radial 4 | 87.5% | 0.274 | 111152 | 86.02% | 86.73% | 86.02% | 8.17 | 6.12 | -1.84% | 84.18%
Radial 5 | 87.2% | 0.203 | 137429 | 86.70% | 86.97% | 86.70% | 5.33 | 9.38 | -2.81% | 83.89%
Radial 6 | 85.5% | 0.035 | 183504 | 87.82% | 86.07% | 86.07% | 3.15 | 15.87 | -4.76% | 81.31%
Radial 7 | 84.4% | 0.038 | 249698 | 91.04% | 85.91% | 85.91% | 1.73 | 28.90 | -8.67% | 77.24%
Radial 8 | 79.9% | 0.006 | 604833 | 165.45% | 84.79% | 84.79% | 0.936 | 53.42 | -16.03% | 68.77%
Radial 9 | 84.2% | 0.004 | 529342 | 175.59% | 87.72% | 87.72% | 0.504 | 99.21 | -29.76% | 57.96%
Radial 10 | 85.8% | 0.003 | 521655 | 194.89% | 88.93% | 88.93% | 0.274 | 182.5 | -54.74% | 34.19%

## Slide 119: Adding efficiency corrections to optimiser
Optimiser doesn’t seem to avoid low-efficiency areas
Last stage efficiency is still 35%
Including Mach number correction seems to break solver
Returns values where inlet radius > outlet radius
Not sure why this is occurring, will investigate more
Case | Total compression energy (kW) | Total compressor weight (kg) | Average efficiency (%)
Baseline | 17.85 | 97.44 | 84.8
Reynolds and tip gap after optimisation | - | - | 72.75
+ Reynolds correction in optimiser | 17.99 | 104.97 | 84.15
+ tip gap correction in optimiser | 22.88 | 139.20 | 72.3
+ Mach correction | Solver breaks! Returns nan |  | 

## Slide 120: Very high level parameter optimisation
Energy usage per day (kWh)
Equivalent system mass (kg-e)

## Slide 121: Results from VHLP optimisation
General behaviour is exactly as expected
  Decreasing mass flow decreases average efficiency, increases energy
    Some radial rotors hitting a 1% efficiency floor!
  Increasing stage number reduces energy – but HX pressure drop limits this
HX optimiser is still not working
  Every Nth optimisation will run off, produce something with >30% pressure drop
  More of a problem for low delta T, high mass flow heat exchangers – not sure why
  Will explore analytic optimum-finding next
Need to iterate a few times to dial in the correct output pressure